# Kuka Youbot Risk Assessment

School Assessment No.	INFRA36
Title of Activity:	Working with Kuka Youbots
Location(s) of Work:	Inspace - Robotics

Hazard Identification: Identify all the hazards; evaluate the risks (low / medium / high); describe all existing control measures and identify any further measures required.

Hazard (s)	Risk / L / M / H	Control Measures (i.e., alternative work methods / mechanical aids / engineering controls, etc.)	Risk / L / M / H
Weight / (lifing injury) / Battery rupture (acid burn) / Tripping	M / M / M	With the manipulator arm the robot weighs around 27kg. / If lifting the robot,use two people, or a lifting aid, to avoid the risk of injury. / If transporting, use a trolley / Due to incorrect usage, shorting, damage or ageing the batteries may rupture, leading to a spillage of acid. / If there is such a spill it should be immediately contained and mopped up and any affected floor tiles removed and washed down. Use rubber gloves to protect the hands and absorbent cloths/paper towels to soak up the spillage. Collect all used materials in a plastic bag for further disposal, do not place in normal waste stream. / The robots are not particularly tall and may not be in the line of sight of inattentive passers by, causing a tripping incident. / Ensure that all those who may enter the working area of the robots are aware of their presence, by marking out the area in use or by verbal warning.	L / L / L

Engineering Controls: Tick relevant boxes

Guarding		Extraction (LEV)		Interlocks		Enclosure
Other relevant information (incl. testing frequency if appropriate):

Personal Protective Equipment (PPE): Identify all necessary PPE.

Eye / Face		Hand /Arm		Feet / Legs		Respiratory
Body (clothing)		Hearing		Other (Specify)
Specify the grade(s) of PPE to be worn: / None required.
Specify when during the activity the item(s) of PPE must be worn:

Non-disposable items of PPE must be inspected regularly and records retained for inspection

# Persons at Risk: Identify all those who may be at risk.

Academic staff	X	Technical staff	X	P’Grad students	X	U’Grad students	X
Maintenance staff	X	Office staff		Cleaning staff		Emergency personnel
Contractors		Visitors	X	Others

Additional Information: Identify any additional information relevant to the activity, including supervision, training requirements, special emergency procedures, requirement for health surveillance etc.

Supervision and training for this robot is at the discretion of the Lab. manager

Assessment carried out by:

Name:	Alejandro Bordallo	Date:	10/6/2016
Signature:		Review Date:	10/6/2017

Checked by Robotics lab manager
Name:	Subramanian Ramamoorthy	Date:
Signature:

# Safe system of work – Form SSW

School Assessment No.	INFRA36
Title of Activity:	Using Kuka Youbots
Location(s) of Work:	Robotics- Inspace

Kuka Youbot / Before use check the battery connections are not damaged. / Never force cables into connection points / If lifting the unit, use two people. / If transporting, use a trolley. Ensure the unit can not move when transported (chock or disable the wheels) / When in operation ensure the work area is clearly marked or their is always an operator present to warn those not involved in the project about the robot’s movement. / Never place the robot where it may cause harm to others (i,e become a tripping hazard, or be in a position to fall on someone) / After use, ensure the unit is powered down and battery disconnected. / For acid leakage from the battery: / Ensure everything is powered down. Disconnect the battery if possible / Cordon off the area . / Obtain rubber gloves and cloths/paper towels from the Cleaner’s closet. / Put on the gloves and contain and mop up the spill. / Contact Technical support and arrange the removal of any affected floor tiles immediately for washing down. / In the event of injury due to acid spill, patient should place burn area under running water and irrigate until symptoms ease. If irritation is not reduced after 10-15 mins seek further medical advice. / The emergency phone number is 2222 / The nearest First Aid box is in the Inspace kitchen / Informatics First Aider list can be found on the web at; / http://www.inf.ed.ac.uk/safety/first-aiders.html / The person responsible for overall safety in the Inspace area is Subramanian Ramamoorthy

School Assessment No.	INFRA36
Title of Activity:	Using Kuka Youbots
Location(s) of Work:	Robotics - inspace

### Verification by users

I may be involved in the task covered by this risk assessment. I have read the assessment and the prescribed safe system of work which I fully understand and hereby undertake to adhere to in the interest of my own health and safety and that of others who may be affected by my actions.

Operatives: / (BLOCK CAPITALS)	Signature:	Counter-signature (superviser):	Date: